## Slide 1: Digital Image Processing
GSP 216

## Slide 2: Digital Image Processing
Pre-Processing – Correcting for radiometric and geometric errors in data
  Geometric Corrections: Image Rectification and Restoration
  Radiometric corrections
  Noise Removal
Image Enhancements – Enhancing images so they are better suited for visual interpretation
  Radiometric Enhancements
  Spatial Enhancements
  Spectral Enhancements

## Slide 3: Pre-Processing
Pre-processing includes the initial processing of raw image data to correct for distortions/errors or to eliminate noise present in the data.
  Geometric Correction
  Radiometric Correction & Calibration
  Noise Removal

## Slide 4: Pre-Processing
Geometric Correction
  Systematic Distortions occur due to the effects of the Earth’s rotation and camera angles etc. These can be easily corrected as they are predictable
  Random Distortions occur due to changing terrain (relief displacement) and variations including sensor altitude
    DEMs and Ground control points (GCPs) used to correct for random distortion

## Slide 5: Pre-Processing
Radiometric Correction
Radiometric correction is done to reduce or correct errors in the digital numbers of images.
Done to improve interpretability and analysis of images and to standardize images.
Particularly useful when comparing scenes over a period of time

## Slide 6: Pre-Processing
Radiometric Correction
Radiance measured by a sensor can vary depending the distance between the Earth and the sun and the altitude of the sun above the horizon at a given location, time of day, and time of year.
Atmospheric Correction to compensate for atmospheric scattering in the image. Improves image contrast

## Slide 7: Pre-Processing
The value recorded at a given pixel includes not only the reflected radiation from the surface, but the radiation scattered and emitted by the atmosphere as well

## Slide 8: Radiometric Correction Process
DN (raw value from the sensor)
At-sensor radiance
Top of the Atmosphere (TOA) Reflectance
Surface Reflectance
Convert DNs to radiance based on the rescaling factors provided in the metadata file
Requires additional information:
Earth-sun distance, Solar zenith angle, exoatmospheric irradiance. Often found in metadata.
Requires knowledge of atmospheric conditions and aerosol properties at the time the image was acquired

## Slide 9: Radiometric Correction Process
DN (raw value from the sensor)
Most image processing software packages have radiometric and atmospheric correction tools
Landsat 8 Image Before (left) and After Correction (right)

## Slide 10: Pre-Processing
Pre-Processed Landsat Data Products
Land Surface Reflectance Products
  Available through EarthExplorer for most Landsat 4-8 scenes
  Radiometric and atmospheric correction have already been applied
Additional products available through the Earth Resources Observation and Science (EROS)
  Top-of-Atmosphere (TOA) radiance
  Top-of-Atmosphere (TOA) reflectance

## Slide 11: Pre-Processing
Noise Removal
  Remove unwanted noise from images
  Destriping
  Random Noise

## Slide 12: Image Enhancements
Radiometric Enhancements
  Contrast Stretching
Spatial Enhancements
  Filters
  Resampling, projecting, etc.
Spectral Enhancements
  False color
  “Band swapping”

## Slide 13: Contrast Stretching
Computer monitors have a range of brightness that they use to display images (0 to 255)
Unprocessed images often don’t use the full range
Contrast stretching improves the contrast of the image by “stretching” the Pixel Values (DNs) to take advantage of the full range

## Slide 14: Contrast Stretching
Low Contrast Better Contrast
“No Stretch” “Stretched”

## Slide 15: Contrast Stretching
Low Contrast Better Contrast
“No Stretch” “Stretched”

## Slide 16: Spatial Filtering
Spatial Filtering is done to emphasize or deemphasize certain features depending on the spatial frequency
Spatial frequency refers to the “roughness” of the tonal variation in the image
Filters can be used to sharpen or emphasize the edges in an image or to smooth an image

## Slide 17: Spatial Frequency
Low High

## Slide 18: Low Pass Filters
Original Image
Low Pass Filter

## Slide 19: High Pass Filter
Original Image
High Pass Filter

## Slide 20: Pan Sharpening
Notes: What is pan sharpening? Pan sharpening uses a higher-resolution panchromatic image (or raster band) to fuse with a lower-resolution multiband raster dataset. The result produces a multiband raster dataset with the resolution of the panchromatic raster, where the two rasters fully overlap. (Esri)