## Slide 1: Remotely Sensed Data
GSP 510
Fall 2023
Dr. Jim Graham
Materials from Sara Hanna

## Slide 2: Remotely Sensed Data
Remotely Sensed data is:
  Acquired remotely from the observer
    This makes it different from field surveys
  Acquired by:
    Satellites
    Airplanes
    UAVs/UAS/Drones
    Automated Stations?

## Slide 3: Active vs. Passive
“Sensors” can be active or passive
  Active sensors send out a signal and measure the returned signal:
    LiDAR
    Radar
  Passive sensors measure energy emitted by another source, usually the sun
    Most of the data we use (except DEMs) are from passive sensors so we’ll be talking about them from now on
For more information, see GSP 216

## Slide 4: Earth Observing Satellites

## Slide 5: Landsat 8 – King Fire
True Color
Notes: The King Fire was a wildfire that scorched over 97,000 acres of land in El Dorado County, California in the fall of 2014

## Slide 6: Landsat 8 - King Fire
False Color (Red – Shortwave Infrared, Green – NIR, Blue – Visible)

## Slide 7: Landsat 8 - King Fire
False Color (Red – Shortwave Infrared, Green – Shortwave Infrared, Blue – NIR)

## Slide 8: Landsat 8 – King Fire October 5, 2014

## Slide 9: Landsat Timeline

## Slide 10: Landsat Orbit
http://www.youtube.com/watch?v=P-lbujsVa2M

## Slide 11: Landsat
The Landsat satellites have carried six different sensor types
Return Beam Vidicon (RBV)
Multispectral Scanner (MSS)
Thematic Mapper (TM)
Enhanced Thematic Mapper (ETM)
Enhanced Thematic Mapper Plus (ETM+)
Operational Land Imager (OLI) and Thermal Infrared Sensor (TIRS)

## Slide 12: Enhanced Thematic Mapper Plus (ETM+)
Enhanced Thematic Mapper Plus (ETM+) | Landsat 7 | Wavelength (micrometers) | Resolution (meters)
 | Band 1 | 0.45-0.52 | 30
 | Band 2 | 0.52-0.60 | 30
 | Band 3 | 0.63-0.69 | 30
 | Band 4 | 0.77-0.90 | 30
 | Band 5 | 1.55-1.75 | 30
 | Band 6 | 10.40-12.50 | 60
 | Band 7 | 2.09-2.35 | 30
 | Band 8 | .52-.90 | 15

## Slide 13: Where to obtain data?
USGS EarthExplorer
  http://earthexplorer.usgs.gov/
USGS Global Visualization Viewer - GLOVIS
  http://glovis.usgs.gov/
USDA Geospatial Data Gateway
  http://datagateway.nrcs.usda.gov/
Open Topography
  https://opentopography.org/
Google Earth Engine
  https://earthengine.google.com/
Lots of other places

## Slide 14: What data products are available?
Landsat Archive
MODIS
Aerial photos
  Historical
  NHAP/NAAP/NAIP
Digital Elevation Models
Canopy Height from LiDAR
Climate Data
Watershed
Land Use/ Land Cover
Soils

## Slide 15: File Sizes
  MODIS Image -11,127,225 pixels (7 bands, 500m resolution)
  Landsat Panchromatic - 234,404,221 pixels (1 band,15 m resolution)
  Landsat Multispectral - 58,532,901 pixels (7 bands, 30m resolution)
  NAIP Image - 261,532,200 pixels (4 bands, 1 m resolution)

## Slide 16: What format ?
Most data is downloaded in a compressed format
Large file sizes
Various file formats
  GeoTIFF common

## Slide 17: Commercial
SPOT – 1986-2014 (1.5 – 20m)
IKONOS – 1999 (1 -4 m)
  Quickbird – 2001 (0.60 - 2.4 m)
  World-View-2 – 2009 (0.46 – 1.84m)
  WorldView-3 – 2014 (0.31 – 3.7 m)
  Disaster Monitoring Constellation (DMC) 2002-Present
    Five satellites, 30-40 m in 3-4 bands
  Others…

## Slide 18: Electromagnetic Radiation
Most remotely sensed data is derived from Electromagnetic Radiation (EMR). This includes:
  Visible light
  Infrared light (heat)
  X-Rays
  Radar
  Etc.
To use RS data we need to review some information on EM