## Slide 1: Key Points
To visualize spatial data on a 2d surface, it must be “Projected
We cannot project spatial data to 2d without some distortion
Common projected systems in the US include:
  Universal Transverse Mercator
  State Plane
  Albers
  Lambert
  Geographic on a 2d surface

## Slide 2
“Projects” spherical data onto a
2d (planar) surface
Map Projections

## Slide 3
Map Projections

## Slide 4
Projection families:
Projection Surface

## Slide 5
Others
Pseudocylindrical
Mollweide
Sinusoidal
Goode Homolosine
Sinusoidal
Goode Homolosine
Projection Surface

## Slide 6
Distortion is unavoidable….
Shape
Area
Distance
Direction
Map Projections
Different map projections exist in order to preserve some properties of the geographic data

## Slide 7: Visualizing distortion: what happens to Justin Bieber?
Notes: Created by Chris Ringo

## Slide 8: Visualizing distortion: what happens to Justin Bieber?
Notes: Mercator is a conformal cylindrical projection, and stretches out higher latitudes

## Slide 9: Visualizing distortion: what happens to Justin Bieber?

## Slide 10: Visualizing distortion: what happens to Justin Bieber?
Notes: Hey, they look the same!
ESRI uses this projection to display a geographic coordinate system

## Slide 11: Visualizing distortion: what happens to Justin Bieber?

## Slide 12: Visualizing distortion: what happens to Justin Bieber?

## Slide 13
Types of projections:
Conformal projections
  Preserve shapes and angles
Equal area projection
Equidistant projections
True-direction projections
Map Projections

## Slide 14
Note the size of Greenland
Greenland: 0.8 million sq. miles
Africa: 11.6 million sq. miles
Mercator
Conformal and True-Direction.
Map Projections
Family: Cylindrical

## Slide 15: Mercator with Tissot Ellipses
Wikipedia
Notes: Note that the shape is preserved, size is not

## Slide 16
In Theory...

## Slide 17
Projecting Latitude and Longitude to UTM:
y = northing = K1 + K2p2 + K3p4, where
K1 = Sk0,
K2 = k0sin21" nu sin(lat)cos(lat)/2
K3 = [k0sin41" nu sin(lat)cos3(lat)/24][(5 - tan2(lat) + 9e'2cos2(lat) + 4e'4cos4(lat)]
x = easting = K4p + K5p3, where
K4 = k0sin1" nu cos(lat)
K5 = (k0sin31" nu cos3(lat)/6)[1 - tan2(lat) + e'2cos2(lat)]
In Reality...

## Slide 18: Web Mercator
LonInRadians=Longitude * 0.01745329252
LatInRadians=Latitude * 0.01745329252
Easting = LonInRadians * 6378137.0
  Multiply by the radius of the earth
Northing = 3189068.5 *
  Log((1+Sin(LatRadians))/(1-Sin(LatInRadians)))
  - This one is more complicated

## Slide 19: Universal Transverse Mercator
North
South
60, 6 degree zones
Notes: Entire world is divided into northern and southern hemispheres and then broken up into 6 degree slices.

## Slide 20: UTM Coordinates
X
Y
500,000 meters
Equator
500,000 Easting (X)‏
4,000,000 Northing (Y)‏
84° N Latitude

## Slide 21
UTM Zone 10 North
Projected Coordinate Systems

## Slide 22: UTM Zones in the CONUS

## Slide 23
For southern zones the northing origin is 10,000,000 meters south of the equator and 500,000 meters west of Central Meridian.
10,000,000 meters south of the equator, Northings = 0
At the equator Northings = 10,000,000.
This ensures that only positive coordinate values are observed for southern UTM zones.
Southern UTM Zones:
Projected Coordinate Systems

## Slide 24: State Plane Coordinate System (SPS or SPCS):
Only applicable in the U.S.
Zones
  Defined by county or state lines.
  Different number of zones for each state.
  Sometimes identified by the Federal Information Processing
  System (FIPS) Codes.
Two basic types of map projections:
  The Lambert conformal Conic (for e – w oriented zones)
    Two standard parallels (secant).
  Transverse Mercator (for n – s oriented zones).
  (Alaska also uses oblique Mercator).
Units: Feet or Meters.
Distance distortions are kept below 1 part in 10,000

## Slide 25: State Plane Zones By State

## Slide 26: Ca
http://www-group.slac.stanford.edu/
California State Plane Zones

## Slide 27: Projections used for State Plane

## Slide 28: California State Plane I
Projection: Lambert_Conformal_Conic
False_Easting: 2000000.00000000
False_Northing: 0.00000000
Central_Meridian: -122.00000000
Standard_Parallel_1: 40.00000000
Standard_Parallel_2: 41.66666667
Latitude_Of_Origin: 39.33333333
Linear Unit: Foot_US

## Slide 29: California State Plane Zone I
-122.000 Longitude
39.333
Latitude
2,000,000, 0
0,0

## Slide 30: Lambert Conformal Conic
Popular for maps of North America.
Georeference.org

## Slide 31: North American Albers Equal Area

## Slide 32: North American Albers Equal Area

## Slide 33
From one projected coordinate system to another (same datums)
Projected Coordinate Systems

## Slide 34
From one projected coordinate system to another (different datums)
Projected Coordinate Systems
“Geographic” transformation

## Slide 35: Spatial Precision Projected Systems
Depends on the units:
  Meters: No fractional digits needed for 1 meter precision
  Feet: No fractional digits needed for 1 meter precision
  Miles:
    5280 feet in a mile ~ 1500 meters in a mile
    Need 4 digits after the decimal for 1 meter precision
  Kilometers:
    1000 meters in a kilometer
    Need 3 digits after the decimal for 1 meter precision

## Slide 36: Finding Coordinates
Go to: http://geonames.usgs.gov/
Search for a name
What format are the coordinates in?
What is the accuracy of the data?